## Slide 1: How to Build Android 5.0 on Zedboard
Noritsuna Imamura

## Slide 2: Agenda
Build FSBL(First Boot Loader) & U-boot
Build Kernel
Make device tree file
Build Android 5.0.2
Setup Zedboard
Notes: という形で進める

## Slide 3: Link List
Android Source Code
  https://github.com/noritsuna/zedroid_manifests.git
Kernel Source Code
  https://github.com/noritsuna/zedroid_device_xilinx_zedboard-kernel.git
boot loader & kernel & Android binaries
  https://github.com/noritsuna/zedroid_device_xilinx_zedboard-images.git
    If you don’t need to build this from source code, please go to “Setup Zedboard” section after these binaries.

## Slide 4
Build FSBL(First Boot Loader) & U-boot

## Slide 5: Download Board Design Files
ANALOG DEVICES
  ADV7511 XILINX EVALUATION BOARDS REFERENCE DESIGN
    http://wiki.analog.com/resources/fpga/xilinx/kc705/adv7511
  File
    http://wiki.analog.com/_media/resources/fpga/xilinx/kc705/cf_adv7511_zed_edk_14_4_2013_02_05.tar.gz
Why need?
  ADV7511 is Video Chip for HDMI on Zedboard. Android requires visual output.
    Android supports virtual display since 4.4. If you don’t need use HDMI display, please skip this section.

## Slide 6: Unpack the downloaded file
Go to “cf_adv7511_zed” dir
Start “system.xmp” file by XPS

## Slide 7: Convert version
Click & Answer “Yes” After Questions

## Slide 8: Check HDMI & Generate Flow Design
Click “Generate BitStream”

## Slide 9: Export Hardware Design to “SDK”
Click “Export SDK”

## Slide 10: Lunch SDK
Click “Export & Lunch SDK”

## Slide 11: Finish to lunch SDK

## Slide 12
Next: Compile U-boot

## Slide 13: Prepare Compiler for u-boot
Download XILINX Compiler(Android NDK is OK)
  PetaLinux with compiler
    http://www.xilinx.com/support/download/index.html/content/xilinx/en/downloadNav/petalinux.html
Set Environments
  export PETALINUX=[path to petaLinux compiler]
  export CCOMPILER=arm-xilinx-eabi-gcc
  export ARCH=arm
  export CROSS_COMPILE=arm-xilinx-eabi-
  export PATH=$PATH:${PETALINUX}/tools/linux-i386/arm-xilinx-gnueabi/bin

## Slide 14: Download & Compile u-boot
Download & Compile
  git clone https://github.com/Xilinx/u-boot-xlnx.git
  cd u-boot-xlnx/
  git checkout -b xilinx-v14.4 xilinx-v14.4
  make zynq_zed_config
  make
After finish to compile u-boot, top directory has “u-boot” file.
  This is u-boot image without hardware info.

## Slide 15
Next: Back to SDK for building boot image

## Slide 16: Create Application Project
Select File -> New -> Application Project

## Slide 17: App Wizard 1/2:
Project Name: FSBL
Target Hardware:
  Hardware Platform: cf_adv7511_zed_hw_platform
  Processor: ps7_cortexa9_0
Click “Next>”

## Slide 18: App Wizard 2/2:
Select “Zynq FSBL”
Click “Finish”

## Slide 19: Created FSBL project

## Slide 20: Create Boot Image 1/4
Select Xilinx Tools -> Create Zynq Boot Image

## Slide 21: Create Boot Image 2/4
Lunch Wizard
Click “Add”

## Slide 22: Create Boot Image 3/4
Lunch Sub-Window
Select:
  Partition type: bootloader
Input:
  File path: [U-boot file]
Click “OK”

## Slide 23: Create Boot Image 4/4
Added your “u-boot” in “Boot image partitions”
Change “Output path”:
  output.bin -> boot.bin
Click “Create Image”

## Slide 24: Created Boot Image
Start compiling automatically
After finish, You get boot image for Zedboard as boot.bin

## Slide 25
Build Kernel

## Slide 26: Prepare Compiler
Download XILINX Compiler(Android NDK is OK)
  PetaLinux with compiler
    http://www.xilinx.com/support/download/index.html/content/xilinx/en/downloadNav/petalinux.html
Set Environments
  export PETALINUX=[path to petaLinux compiler]
  export CCOMPILER=arm-xilinx-eabi-gcc
  export ARCH=arm
  export CROSS_COMPILE=arm-xilinx-eabi-
  export PATH=$PATH:${PETALINUX}/tools/linux-i386/arm-xilinx-gnueabi/bin

## Slide 27: Download & Compile Kernel
Download & Compile Kernel
  git clone https://github.com/noritsuna/zedroid_device_xilinx_zedboard-kernel.git
  cd zedroid_device_xilinx_zedboard-kernel
  git checkout zedroid-5.0.2_r1
  make zynq_zed_android_defconfig
  make uImage LOADADDR=8000
You can get “uImage” in “arch/arm/boot/”

## Slide 28
Make device tree file

## Slide 29: Build device tree file
Build device tree file
  cd [kernel dir]
  make zynq-zed-adv7511.dtb
You can get “zynq-zed-adv7511.dtb” in “arch/arm/boot/dts/”
  Rename “zynq-zed-adv7511.dtb” to “devicetree.dtb”

## Slide 30
Build Android 5.0.2

## Slide 31: Download source code & build
Install build tools following Google Android Site
  https://source.android.com/source/downloading.html
Download source code & build
  repo init -u https://github.com/noritsuna/zedroid_manifests -b zedroid-5.0.2_r1
  repo sync
  source ./build/envsetup.sh
  lunch zedboard-userdebug
  make

## Slide 32: Appendix: OpenGL/ES support
If you use “lunch zedboard-userdebug”, this Android is for OpenGL/ES 2.0.
  Zedboard doesn’t have GPU. My Android uses software renderer. It’s soooooooo slow.
  If you use OpenGL/ES 1.2, it’s better to use.
    Android’s OpenGL/ES current version is “2.0”. Some applications require “2.0”.
Special Options
  OpenGL/ES 1.2 version
    lunch zedboard_GLES12-userdebug
  OpenGL/ES 2.0 version
    lunch zedboard_GLES20-userdebug

## Slide 33: Mark up ARM RAM image info
Android’s RAM image is NOT for u-boot.
  sudo apt-get install u-boot-tools
  mkimage -A arm -O linux -T ramdisk -a 0x2000000 -n "Zedboard ramdisk" -d [Android output dir]/ramdisk.img uramdisk.image.gz
  “uramdisk.image.gz” file is RAM image for u-boot.

## Slide 34
Setup Zedboard

## Slide 35: Prepare Hardwares: SD Card 1/2
4GB SD Card
  Partition:
    1st primary: VFAT(FAT32) over 1GB with boot flag
    2nd primary: ext4 over 1GB
    3rd primary: ext4 over 500MB
    4th primary: Linux Swap over 500MB
  Copy Files
    [Xilinx SDK dir]/boot.bin
    [kernel dir]/arch/arm/boot/uImage
    [kernel dir]/arch/arm/boot/dts/devicetree.dtb
    [Android dir]/uramdisk.image.gz
      To 1st partition

## Slide 36: Prepare Hardwares: SD Card 2/2
4GB SD Card
  Copy Files
    [Android output dir]/system/* files with permission info
      To 2nd partition
    [Android output dir]/userdata/* files with permission info
      To 3rd partition

## Slide 37: Prepare Hardwares: Zedboard DIPs
JP2, JP3, JP6: “Short”
JP18: “1V8” is “Short”
MI02, MI03, MI06: “3V3” is “Short”
MI04, MI05: “GND” is “Short”

## Slide 38: Prepare Hardwares: LAN, HDMI, OTG
Required LAN, HDMI
  If you don’t connect them, it doesn’t boot up.
Required 2 more ports: USB Hub
  USB port is OTG only. Other USB port is NOT USB.

## Slide 39: Power ON!
Insert SD Card
Connect AC Adapter and Turn on Power Switch!
  Please wait 5-10 mins. Because when 1st boot, ART compile all applications to native binary.
Enjoy!